# Prozeduale CAD- Modelle erstellen mit CadQuery
CadQuery ist eine Python- Bibliothek, die auf dem Datenmodell von FreeCAD aufsetzt und es ermöglicht, mit Python 3D- CAD- Modelle zu erzeugen.
Jedenfalls in der Theorie.. In der Praxis sind selbst scheinbar simple Operationen ein tagelanges Try & Error, um was man aber nicht wirklich umrumkommt, wenn man z.B. aus Parameterlisten komplexe Bohrlochplatten machen will.
So entstand unter Schmerzen letztlich dieses Programm (im QC-Editor), was Bohrlöcher anhand einer Parameterliste setzt:
import cadquery as cq plate_width=200.0 /1000.0 plate_height=150.0 /1000.0 thickness=30.0 /1000.0 m3_hole = 3.5 m3_head = 5.5 m3_depth = 20.0 connectors={ # this is a kind of library for the different connector footprints "MGW":[ # each connector has one or more areas of a pin grid { #where each area has a position inside the connector # its relative position inside the connector "x":0.1, "y":0.1, # and a set of column dimensions, relative to each other "cols":[6.5,8.5, 8.5], #the related row dimensions "rows":[7.45, 9.9, 18.2], #""rows":[7.45, 9.9, 8.2], # and then finally the property for each pin # the hole diameter, the borehole diameter, # the borehole depth, the long hole length, # the long hole diameter and the long hole orientation # if long hole diameter or length is 0, the hole is not made "pins":[ # first row [m3_hole, m3_head, m3_depth, 3.0, 3.0, "v"], [m3_hole, m3_head, m3_depth, 6.5, 3.0, "v"], [m3_hole, m3_head, m3_depth, 3.0, 3.0, "v"], # second row [m3_hole, m3_head, m3_depth, 6.5, 3.0, "v"], [m3_hole, m3_head, m3_depth, 6.5, 3.0, "h"], [m3_hole, m3_head, m3_depth, 6.5, 3.0, "v"], # third row [m3_hole, m3_head, m3_depth, 3.0, 3.0, "v"], [m3_hole, m3_head, m3_depth, 8.0, 3.0, "h"], [m3_hole, m3_head, m3_depth, 3.0, 3.0, "v"], ] } ] } plate=[ # a number of connectors { #each connector consists of "x":20.0, "y":0.0, "type":"MGW" }, { #each connector consists of "x":100.0, "y":0.0, "type":"MGW" }, ] x_offset=-plate_height/2 y_offset=-plate_width/2 # make the base print("box:",plate_height, plate_width , thickness) result = cq.Workplane("XY").box(plate_height, plate_width , thickness) for single_connector in plate: connector=connectors[single_connector["type"]] connector_x=single_connector["x"] /1000 connector_y=single_connector["y"] /1000 for area in connector: area_x=area["x"] /1000 + connector_x area_y=area["y"] /1000 + connector_y print("area",area_x,area_y) rows=area["rows"] cols=area["cols"] row_count=len(rows) col_count=len(cols) #row_pos=area_x row_pos=area_y for row_index in range(row_count): row_pos += (rows[row_index] /1000) #col_pos = area_y col_pos = area_x for col_index in range(col_count): col_pos += cols[col_index]/1000 pin_index= row_index * col_count + col_index print("pin pos", pin_index, row_pos, col_pos) pin=area["pins"][pin_index] print(pin) pin_hole_size=pin[0] /1000 /2 # diameter -> radius pin_screw_size=pin[1] /1000 /2 # diameter -> radius pin_screw_depth=pin[2] /1000 pin_slot_length=pin[3] /1000 pin_slot_width=pin[4] /1000 pin_type=pin[5] # aus purer verzweiflung: Vertauschen von x und y :-( x_pos, y_pos= row_pos, col_pos #wp.center(row_pos,col_pos).hole(5.0) result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset, y_pos +y_offset ).circle(pin_hole_size).cutThruAll() result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset, y_pos +y_offset ).circle(pin_screw_size).cutBlind(pin_screw_depth) if pin_slot_length> 0 and pin_slot_width>0: if pin_type.lower()=="v": result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset, y_pos +y_offset ).move( -pin_slot_length,-pin_slot_width/2).lineTo(pin_slot_length,-pin_slot_width/2).lineTo(pin_slot_length,pin_slot_width/2).lineTo(-pin_slot_length,pin_slot_width/2).close().cutBlind(pin_screw_depth) result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset + pin_slot_length, y_pos +y_offset ).circle(pin_slot_width / 1.99 ).cutBlind(pin_screw_depth) result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset - pin_slot_length, y_pos +y_offset ).circle(pin_slot_width / 1.99 ).cutBlind(pin_screw_depth) else: result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset, y_pos +y_offset ).move(-pin_slot_width/2, -pin_slot_length).lineTo(-pin_slot_width/2,pin_slot_length).lineTo(pin_slot_width/2,pin_slot_length).lineTo(pin_slot_width/2,-pin_slot_length).close().cutBlind(pin_screw_depth) result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset , y_pos +y_offset + pin_slot_length).circle(pin_slot_width / 1.99 ).cutBlind(pin_screw_depth) result = result.workplane(offset=0, centerOption="CenterOfBoundBox").center(x_pos + x_offset , y_pos +y_offset - pin_slot_length).circle(pin_slot_width / 1.99 ).cutBlind(pin_screw_depth) # Render the solid show_object(result) cq.exporters.export(result,'/media/ram/result.stl') cq.exporters.export(result.section(),'/media/ram/result.dxf')