# Fritzbox Call Monitor with ESP8266
At start it was just a question of a relevant, if it could not be indicated somehow, that there's a phone call ongoing on the Fritzbox.
When thinking about it, the first idea was to do something with the TR-064 protocol, but in the end it's much more simple:
When activated with the special phone number
#96*5*
the Fritzbox reports SIP information on port 1012 like this
20.02.16 18:28:24;RING;0;017xxxxxxxx;8xxxxxx;SIP1;
20.02.16 18:28:27;DISCONNECT;0;0;
20.02.16 18:29:03;CALL;1;12;9xxxxx;053xxxxxx;SIP2;
20.02.16 18:29:31;CONNECT;1;12;053xxxxxx;
20.02.16 18:29:52;DISCONNECT;1;21;
20.02.16 18:30:00;CALL;1;12;9xxxxx;053xxxxxx;SIP2;
20.02.16 18:30:18;CONNECT;1;12;053xxxxxx;
20.02.16 18:51:39;DISCONNECT;1;1281;
20.02.16 18:58:12;CALL;1;11;9xxxxx;041xxxxxxxxx;SIP2;
20.02.16 18:58:26;DISCONNECT;1;0;
This information can be viewed under linux simply with
netcat fritz.box 1012
## Implementation on a ESP8266
As a quick and dirty solution, I took a TCP client sample and modified it to connect first to Wifi, then to the Fritzbox and then listen to the incoming status messages.
Whenever a CONNECT or DISCONNECT is discovered, the build-in LED is switched on or off.
Job done…
#include <ESP8266WiFi.h> const char* ssid = "yourWiFiSSID"; const char* password = "yourpassword"; const char* host = "192.168.2.1"; const char *connect = ";CONNECT"; const char *disconnect = ";DISCONNECT"; // for Wemos D1 #if 0 #define OUTPUT_PIN (2) #define OUT_ON LOW #define OUT_OFF HIGH #else // for OBI Socket 2 #define OUTPUT_PIN (4) #define OUT_ON HIGH #define OUT_OFF LOW #endif void setup() { pinMode(OUTPUT_PIN, OUTPUT); // Initialize GPIO pin as an output Serial.begin(115200); Serial.println(); Serial.printf("Connecting to %s ", ssid); WiFi.begin(ssid, password); while (WiFi.status() != WL_CONNECTED) { delay(500); Serial.print("."); } Serial.println(" connected"); digitalWrite(OUTPUT_PIN, OUT_ON); // Turn the LED on delay(500); // Wait for 500 ms digitalWrite(OUTPUT_PIN, OUT_OFF); // Turn the LED off } void loop() { WiFiClient client; Serial.printf("\n[Connecting to %s ... ", host); if (client.connect(host, 1012)) { Serial.println("connected]"); /* Serial.println("[Sending a request]"); client.print(String("GET /") + " HTTP/1.1\r\n" + "Host: " + host + "\r\n" + "Connection: close\r\n" + "\r\n" ); Serial.println("[Response:]"); */ while (client.connected() || client.available()) { if (client.available()) { String line = client.readStringUntil('\n'); Serial.println(line); if( line.indexOf( connect ) > -1) { Serial.println("line busy]"); digitalWrite(OUTPUT_PIN, OUT_ON); // Turn the OUTPUT on } if( line.indexOf( disconnect ) > -1) { Serial.println("line free]"); digitalWrite(OUTPUT_PIN, OUT_OFF); // Turn the OUTPUT off } } } client.stop(); Serial.println("\n[Disconnected]"); } else { Serial.println("connection failed!]"); client.stop(); } delay(5000); }