# Pipimat 2000 - Die Teppichnässer- Alarmanlage
Klingt komisch, is aber so: Diese Schaltung macht MP3- Radau, wenn die Sensormatte einen vierbeinigen Mitbewohner dabei erwischt, dass er mal wieder seine Reviermarke in den Teppich setzt.
## Installation von Circuit Python
Wenn der Pico sich am Rechner nicht als USB-Drive zeigt: Beim Einstecken den BOOTSEL- Button so lange gedrückt halten, bis das Laufwerk erkannt wird.
Dann das aktuelle UF2 File von circuitpython homepage herunterladen und durch Drag & Drop auf dem Pico installieren.
Der Pico wird dann neu booten und sich als CIRCUITPI neu anmelden.
Dann wird der Audio-Anteil verkabelt wie auf https://learn.adafruit.com/mp3-playback-rp2040 gezeigt:
Signal	Pico	Pin
PAM8302 A+	GP0	1
PAM8302 A-	GND	3
PAM8302 VIN	VBUS (USB 5V)	40
PAM8302 GND	GND	23

Für's Audio- Signal Audio- Signal brauchen wir MP3 Mono 16Bit PCM max. 24kHz Sample Rate. Wie man das mit Audacity hinbekommt, steht auf https://learn.adafruit.com/microcontroller-compatible-audio-file-conversion
## Das Programm
import board
import audiomp3
import audiopwmio
import time
import analogio
import digitalio
led = digitalio.DigitalInOut(board.LED)
led.direction = digitalio.Direction.OUTPUT
led.value = True
# Set up an analog input on ADC0 (GP26), which is physically pin 31.
# E.g., this may be attached to photocell or photointerrupter with associated pullup resistor.
sensor = analogio.AnalogIn(board.A0)
alarm = False
supress_alarm= False
lower_threshold = 50000
upper_threshold = 55000
button = digitalio.DigitalInOut(board.GP2)
button.switch_to_input(pull=digitalio.Pull.UP)
audio = audiopwmio.PWMAudioOut(board.GP0)
decoder = audiomp3.MP3Decoder(open("trash.mp3", "rb"))
while True:
    if alarm:
        led.value = not led.value
    else:
        led.value = True
    # Read the sensor once per cycle.
    sensor_level = sensor.value
    # uncomment the following to print tuples to plot with the mu editor
    print(sensor_level)
    if alarm:
        if sensor_level > upper_threshold:
        led.value = False
        alarm = False
        print("Off")
    else:
        supress_alarm=False
        if sensor_level < lower_threshold:
        led.value = True
        alarm = True
        print("On")
    if not button.value:
        audio.play(decoder)
        while audio.playing:
        pass
        print("Done playing!")
    if alarm and not supress_alarm:
        audio.play(decoder)
        while audio.playing:
        if not button.value:
        supress_alarm=True
        audio.stop()
        # comment the next line if the alarm shall run endless
        #supress_alarm=True
        print("Done alarm playing!")
    time.sleep(1) # slow sampling to avoid flooding